## Slide 1: Design verification using Specman
Instruction for interfacing specman with Modelsim

## Slide 2: Install Specman
1. Get a Specman installation packet from somewhere or you can get a cracked one from us.
2. Making sure you have all tar files:

## Slide 3: Run installation script
Using sh ./sn_5.0_install.sh -64bit command to run the installation script. (Recommand try it on engineering computer lab)
Choosing completely install.

## Slide 4: Setup environment parameter
1. Setup VRST_HOME
setenv VRST_HOME /path_where_you_install
source $VRST_HOME/env.csh -64bit
2. Setup SPECMAN_HOME
source $VRST_HOME/env.csh SPECMAN_HOME=sn_5.0
3. Setup LM_LICENSE_FILE
source $VRST_HOME/env.csh LM_LICENSE_FILE= /path

## Slide 5: Run specman

## Slide 6: verify.sh
specman -command "load design; write stubs -verilog;“
vlib work
vlog specman.v design.v
cmd = "";
cmd="vsim -keepstdout -c topMod specman";
$cmd <<EOF
Sn
load design.e;
Test
run 10000EOF

## Slide 7: design.v
adder
Fadder
syn_clk
topMod

## Slide 8: design.e
unit testDut
function verify()
struct operation