## Slide 1
FPGA Design flow using PlanAhead
Mahmoud Sadollahi
Vahid Behravan

## Slide 2
What is FPGA ?
2
7/6/2013
A field-programmable gate array (FPGA) is an integrated circuit designed to be configured by a customer or a designer after manufacturing

## Slide 3
FPGA manufacturers
3
7/6/2013
Xilinx and Altera two major FPGA manufacturers
2010 market share: (reference : sourcetech411.com)
2012 market share: Xilinx 47% , Altera 41%

## Slide 4
FPGA programming tools
4
7/6/2013
Xilinx : ISE , PlanAhead , …
Altera : Quartus II

## Slide 5
Xilinx FPGA families
5
7/6/2013
CPLD, SPARTAN, VIRTEX, KINTEX, ARTIX, …
Features | Artix-7 | Kintex-7 | Virtex-7 | Spartan-6 | Virtex-6
Logic Cells | 215,000 | 480,000 | 2,000,000 | 150,000 | 760,000
BlockRAM | 13Mb | 34Mb | 68Mb | 4.8Mb | 38Mb
DSP Slices | 740 | 1,920 | 3,600 | 180 | 2,016
DSP Performance (symmetric FIR) | 930GMACs | 2,845GMACs | 5,335GMACs | 140GMACs | 2,419GMACs
Transceiver Count | 16 | 32 | 96 | 8 | 72
Transceiver Speed | 6.6Gb/s | 12.5Gb/s | 28.05Gb/s | 3.2Gb/s | 11.18Gb/s
Total Transceiver Bandwidth (full duplex) | 211Gb/s | 800Gb/s | 2,784Gb/s | 50Gb/s | 536Gb/s
Memory Interface (DDR3) | 1,066Mb/s | 1,866Mb/s | 1,866Mb/s | 800Mb/s | 1,066Mb/s
PCI Express® Interface | x4 Gen2 | x8 Gen2 | x8 Gen3 | x1 Gen1 | x8 Gen2
Analog Mixed Signal (AMS)/XADC | Yes | Yes | Yes |  | Yes
Configuration AES | Yes | Yes | Yes | Yes | Yes
I/O Pins | 500 | 500 | 1,200 | 576 | 1,200
I/O Voltage | 1.2V, 1.35V, 1.5V, 1.8V, 2.5V, 3.3V | 1.2V, 1.35V, 1.5V, 1.8V, 2.5V, 3.3V | 1.2V, 1.35V, 1.5V, 1.8V, 2.5V, 3.3V | 1.2V, 1.5V, 1.8V, 2.5V, 3.3V | 1.2V, 1.5V, 1.8V, 2.5V
EasyPath Cost Reduction Solution | - | Yes | Yes | - | Yes
FPGA Comparison Table

## Slide 6
Planahead Overview
6
7/6/2013
PlanAhead is a tool for performance improvement of design.
When you use all HDL coding techniques for performance improvement and you don’t achieve the goals, PlanAhead can help.
It is usually useful for design over 150MHz.
Xilinx has a plan to replace ISE by PlanAhead from version 15 of ISE.

## Slide 7
Overview (Cont.)
7
7/6/2013
PlanAhead basically can do everything that ISE can do, including synthesis and implementation.
It has a better GUI than ISE and also more suitable for timing analyzing and performance improvement of design.
It includes some features not available in ISE and user can use them to do performance evaluation/improvement more easily.
RTL Developing
Create Netlist
Implementation (PAR)
RTL Analysis
Netlist
Analysis
Impl.
Analysis
Floorplanning

## Slide 8
RTL Analysis
8
7/6/2013
analyze the RTL logic hierarchy
RTL schematic
RTL resource estimations
RTL power estimations
run an RTL Design Rule Check (DRC).

## Slide 9
Netlist Analysis
9
7/6/2013
Design statistics
Hierarchical viewer
Schematic viewer
Timing report (estimation)
DRC

## Slide 10
Implementation Analysis
10
7/6/2013
Design statistics
Hierarchical viewer
Schematic viewer
Timing report and critical path viewer
DRC
Connectivity
Floorplanning

## Slide 11
Design statistics
11
7/6/2013

## Slide 12
Hierarchical viewer
12
7/6/2013

## Slide 13
Schematic viewer
13
7/6/2013

## Slide 14
Connectivity
14
7/6/2013

## Slide 15
Connectivity (Cont.)
15
7/6/2013

## Slide 16
Critical path viewer
16
7/6/2013

## Slide 17
Implementation Analysis
17
7/6/2013
Defining area for each block (module) can be done with adding some lines in UCF file.

## Slide 18
Floorplanning
18
7/6/2013

## Slide 19
Summary
19
7/6/2013
When all HDL coding techniques don’t help to achieve desired performance, there is one more way: Floorplanning.
For Floorplanning we need to make a very important decision: which block or blocks are good candidates for floorplanning?: PlanAhead helps designer to make this decision.
Floorplannig is an iterative procedure.

## Slide 20
20
7/6/2013
Thank You